# Arc Buddy Tutorial #2
This is a slightly more advanced tutorial for cutting an arc with G Codes.

If you want to make a part like this one and need to cut the arc for the curved slot you can use Arc Buddy to generate the G code needed.

Using the drawing at the left you can see the first tool path you need to generate. The X and Y centers will depend on your part. First lay out the slot then lay out the tool path based on the diameter of your tool. Remember to use angles starting with 0 on the right and going CCW.

You don't need a fancy cad drawing to figure this out. You need to move to the starting point with your tool then cut the arc. If you run in the sim mode (machine off) as you do each arc you can see if your ending point is correct for the starting point of the next arc. Generate each arc in order of cut. Now try and generate the rest of the tool path. The outside edge of the slot is 10.0000. Try this before going on to the next page.